## Slide 1: Pressure Prediction by a Convolutional Neural Net
Jacob Child

## Slide 2: Motivation
Clearly defines the problem, provides context, and explains significance.
Particle Image Velocimetry- An experimental method that returns velocity fields, and pressure fields can only be predicted through estimating boundary conditions and then using computationally expensive numerical methods
Super-resolution and denoising of fluid flow using physics-informed convolutional neural networks without high-resolution labels (The HW 8 Paper) –

## Slide 3: Particle Image Velocimetry
A laser sheet is shined through a particle laden flow
Two highspeed images are taken in quick succession
A computer is used to track the particle movement and create a velocity field
No pressure data
Used with permission

## Slide 4: Relevant Literature
ResearchRabbit suggested paper collection (not curated)

## Slide 5: Approach: Vascular Flow (done in class)
Convolutional Neural Net to upscale x and y components of velocity, also predict a pressure field
Governing Equations: x and y momentum from 2D Navier-Stokes, continuity from 2D Navier Stokes
Incorrect pressure field
  “The current framework cannot accurately recover the hidden pressure field because of the implicit coupling of pressure and velocity (i.e., the pressure appears as a source term in the momentum equations). The governing equation needs to be reformulated to strongly couple the pressure and velocity predictions based on, e.g., elliptic equation of pressure 81 and Rhie–Chow interpolation.75”

## Slide 6: Methods
Uses appropriate methods and best practices. Explains approach with technical rigor (e.g., model architecture, loss functions, training details).

## Slide 7: Methods
Convolutional Neural Net: Good for spatially correlated data (flow fields)
  Activation Function: ReLU
  Layer Channels: 2 (input) -> 16 -> 32 -> 64 -> 32 -> 3 (output)
  Kernel Size: 5x5
  Padding: 2
  Learning Rate: 1e-3, or 1e-4
Copied and modified the paper slightly- produced satisfactory results

## Slide 8: Layout
Super-resolution: upscale and predict u, v, p
Super-resolution: give the upscaled data and predict p
PIV Side-View Dataset: predict p
PIV Wake-View Dataset: predict p

## Slide 9: Super-Resolution
Predicting: u, v, p
Enforced Boundary Conditions
Code

## Slide 10: Loss Functions (Super-resolution for u, v, p)
Assumptions: Incompressible, steady, constant density
Continuity:
X-Momentum
Y-Momentum

## Slide 11: Results
Original, 5000 epochs, no extra pressure term

## Slide 12: Pressure Poisson (Elliptic Equation of Pressure)
Pressure Poisson:
Wikipedia: Pressure Poisson
Barba Group: Code Application

## Slide 13: Results
Original, 10000 epochs, pressure poisson

## Slide 14: Super-Resolution
Predicting: p
No Boundary Conditions
Code

## Slide 15: Results
5000 epochs, pressure poisson
5000 epochs, pressure poisson, “pitot data”

## Slide 16: Results
10000 epochs, pressure poisson , “pitot data”
10000 epochs, pressure poisson, “pitot data” on the boundaries

## Slide 17: PIV Side-View
Predicting: p
Code

## Slide 18: Input

## Slide 19: CFD Comparison data

## Slide 20: Results
5000 epochs, pressure poisson , pitot data

## Slide 21: Results
5000 epochs, pressure poisson , pitot data

## Slide 22: Results
Big Model: Double the number of channels for each layer

## Slide 23: PIV Wake-View
Predicting: p
Code

## Slide 24: Input

## Slide 25: Z-Component of Velocity (w)

## Slide 26: Results
5000 epochs, pressure poisson , pitot data

## Slide 27: Results
5000 epochs, pressure poisson , pitot data

## Slide 28: Results
5000 epochs, pressure poisson , pitot data
u, v, w
u, v

## Slide 29: Conclusions
It is possible to create a semi-accurate pressure field using a physics informed convolutional neural net
Pressure requires some reference value “pitot data”
Boundary values/conditions are more influential than mid-field values
Tip vortices are captured well in the side-view predicted pressure field
The side-view predicted pressure field matches cfd in form but is off in magnitude
The wake-view predicted pressure field is assisted by the Z-component of velocity

## Slide 30: Improvements/Future Work
Pitot Probe pressure data is time averaged, PIV is largely unsteady and CFD is unsteady
For the full benefit of the Z-Component of velocity two Z-planes of PIV data are necessary for derivatives in the z direction
Phase/Tip Vortex mismatch for Wake-View PIV and CFD data
Use the same process on the CFD u, v, w data to further verify the model

## Slide 31: Acknowledgments
Dr. Andrew Ning: teacher, derivative code, other template code
Nathan Welker: PIV data, understanding
AI: Coding assistance